## Slide 1
THE UNIVERSITY OF DODOMA
College of Informatics and Virtual Education
PROJECT 15 · ATmega32 EMBEDDED SYSTEMS
LCD-Based Menu Navigation &
Parameter Setting System
A microcontroller-based embedded user interface for displaying information and configuring system parameters using a 16×2 LCD, push-button menu control, LEDs, and a buzzer.
SN | STUDENT NAME | STUDENT REG_NO
1 | KHADIJA FADHILI ZAHARANI | T23-03-10509
2 | TUMAINI JONAS MABAMBA | T23-03-12131
3 | JUNIOR AMOS RWEZAURA | T23-03-20552
4 | CLEA CHRISTOPHER BINAMUNGU | T23-03-15902

## Slide 2
UNIVERSITY OF DODOMA
PRESENTATION ROADMAP
Outline
LCD-Based Menu Navigation & Parameter Setting System
02 / 20
1
Introduction & Background
2
Problem Statement
3
Project Objectives
4
System Overview
5
Expected System Operation
6
Hardware Components
7
ATmega32 Pin Mapping
8
Circuit Design (KiCad)
9
PCB Layout & Gerbers
10
Firmware Development
11
LCD Interfacing (4-bit)
12
Menu State Machine
13
Button Handling & Debounce
14
SimulIDE Simulation
15
Troubleshooting Notes
16
Assessment Criteria
17
GitHub Submission
18
Extension: EEPROM
19
Conclusion
20
Q & A / References

## Slide 3
UNIVERSITY OF DODOMA
CONTEXT
Introduction & Background
LCD-Based Menu Navigation & Parameter Setting System
03 / 20
Embedded systems are everywhere — in appliances, instruments, and industrial controllers. Most of them need a simple way for a user to see information and change settings.
A display shows the system status, while push buttons let the user move through menus and adjust parameter values. This human-machine interface (HMI) is a core building block of embedded design.
This project applies these ideas on the ATmega32 microcontroller, following the University of Dodoma problem-based learning (PBL) flow: from system operation to hardware, design, firmware, simulation, and demonstration.
Everyday examples
Digital clocks
Temperature controllers
Motor-speed controllers
Counters & alarm systems
Measurement devices

## Slide 4
UNIVERSITY OF DODOMA
THE CHALLENGE
Problem Statement
LCD-Based Menu Navigation & Parameter Setting System
04 / 20
Many embedded systems require a simple, reliable user interface for displaying information and changing system settings — but building one demands correct LCD control, dependable button reading, and clear menu logic.
Display Control
Drive a 16×2 LCD correctly in 4-bit mode and show menus and values without garbage characters.
Input Reading
Read five push buttons reliably, with debouncing to avoid false or repeated presses.
Menu Logic
Manage states — welcome, menu, edit, save, error — and update the display on every change.

## Slide 5
UNIVERSITY OF DODOMA
WHAT WE AIM TO ACHIEVE
Project Objectives
LCD-Based Menu Navigation & Parameter Setting System
05 / 20
Main Objective
To design and implement an LCD-based menu navigation and parameter setting system using ATmega32 GPIO pins, a 16×2 LCD, push buttons, LEDs, and a buzzer.
Specific Objectives
Interface a 16×2 LCD in 4-bit mode with the ATmega32.
Read and debounce five push-button inputs.
Implement a navigable menu with at least one adjustable parameter.
Provide LED and buzzer feedback for confirmation and errors.
Design the schematic and PCB in KiCad and verify in SimulIDE.
Document and submit the project on GitHub.

## Slide 6
UNIVERSITY OF DODOMA
ARCHITECTURE
System Overview
LCD-Based Menu Navigation & Parameter Setting System
06 / 20
The ATmega32 sits at the centre, reading buttons and driving the LCD, LEDs, and buzzer.
ATmega32
5 Push Buttons
5V Supply
16×2 LCD
2 Status LEDs
Buzzer
Inputs
Controller
Outputs

## Slide 7
UNIVERSITY OF DODOMA
BEHAVIOUR SPECIFICATION
Expected System Operation
LCD-Based Menu Navigation & Parameter Setting System
07 / 20
Power ON
LCD shows welcome message
Menu pressed
Main menu is displayed
Up pressed
Cursor moves upward
Down pressed
Cursor moves downward
Select pressed
Selected menu item opens
Increase pressed
Parameter value increases
Save pressed
LCD shows “VALUE SAVED”
Invalid action
Buzzer gives error beep
Reset pressed
Returns to welcome screen

## Slide 8
UNIVERSITY OF DODOMA
BILL OF MATERIALS
Hardware Components
LCD-Based Menu Navigation & Parameter Setting System
08 / 20
ATmega32 MCU
Main controller running firmware
×1
16×2 LCD Module
Displays menu & parameter values
×1
Push Buttons
Menu, Up, Down, Select, Save
×5
Status LEDs
Status & mode indication
×2
Buzzer
Audio feedback (confirm / error)
×1
Potentiometer
LCD contrast adjustment
×1
Reset Button
Manual microcontroller reset
×1
5V Power Supply
Powers the whole circuit
×1

## Slide 9
UNIVERSITY OF DODOMA
ATMEGA32 GPIO
Pin Mapping
LCD-Based Menu Navigation & Parameter Setting System
09 / 20
Pin | Function | Connected Device
PC0 – PC1 | Digital output | LCD RS, LCD EN
PC2 – PC5 | Digital output | LCD D4, D5, D6, D7
PA0 – PA2 | Digital input | Menu, Up, Down buttons
PA3 – PA4 | Digital input | Select, Save/Increase
PB0 – PB1 | Digital output | Status LED, Mode LED
PB2 | Digital output | Buzzer
Register Setup
DDRC = 0x3F;
// LCD outputs
DDRA = 0x00;
// button inputs
DDRB = 0x07;
// LED + buzzer
4-bit LCD mode keeps the pin count low.

## Slide 10
UNIVERSITY OF DODOMA
KICAD · SCHEMATIC
Circuit Design
LCD-Based Menu Navigation & Parameter Setting System
10 / 20
The complete schematic connects the ATmega32 to all peripherals with clear net labels.
ATmega32
All LCD, button, LED & buzzer pins shown clearly.
LCD Module
RS, EN, D4–D7, VCC, GND and contrast pin.
Contrast Circuit
Potentiometer wired to set LCD contrast (V0).
Push Buttons
Menu, Up, Down, Select, Save/Increase.
Reset Circuit
Reset push button with pull-up resistor.
Net Labels
LCD_RS, LCD_EN, BTN_MENU, STATUS_LED, BUZZER.

## Slide 11
UNIVERSITY OF DODOMA
KICAD · PCB
PCB Layout & Gerbers
LCD-Based Menu Navigation & Parameter Setting System
11 / 20
Board Outline
Simple rectangular PCB outline defined.
Component Placement
LCD connector & buttons placed for easy access.
Routing
LCD, GPIO, power and ground traces routed.
Silkscreen Labels
Labels for LCD pins, buttons, LEDs & buzzer.
Contrast Access
Potentiometer placed where it is easy to adjust.
Design Checks
ERC & DRC passed; Gerber files generated.

## Slide 12
UNIVERSITY OF DODOMA
MPLAB · FIRMWARE
Firmware Development
LCD-Based Menu Navigation & Parameter Setting System
12 / 20
Firmware written in C configures the hardware and runs the menu logic.
Configure GPIO: LCD outputs, button inputs, LED/buzzer outputs
Initialise the LCD in 4-bit mode
Display the welcome screen at startup
Continuously read the five control buttons
Debounce inputs to reject false readings
Handle menu states and adjust parameters
Drive LEDs and buzzer for feedback
Core structure
System_Init();
Show_Welcome();
while(1){
read_buttons();
update_state();
refresh_lcd();
}

## Slide 13
UNIVERSITY OF DODOMA
DISPLAY DRIVER
LCD Interfacing (4-bit Mode)
LCD-Based Menu Navigation & Parameter Setting System
13 / 20
The HD44780 LCD is driven over four data lines to save pins. Data transfers as two nibbles.
Command / Data
→
LCD Data Pins
→
Enable Pulse
→
LCD Updates
Proper wake-up sequence
Three 0x03 nibbles then 0x02 switch the LCD into 4-bit mode reliably.
Clear command handling
Function set, display on/off, entry mode, clear and cursor positioning.
Padded printing
Fixed-width printing clears leftover characters from previous screens.

## Slide 14
UNIVERSITY OF DODOMA
CONTROL LOGIC
Menu State Machine
LCD-Based Menu Navigation & Parameter Setting System
14 / 20
WELCOME
1
MAIN MENU
2
PARAMETER EDIT
3
VALUE SAVED
4
State transitions
MENU button moves from Welcome to Main Menu.
UP / DOWN scroll through parameters in the menu.
SELECT opens the parameter edit screen.
UP / SAVE increase the value; DOWN decreases it.
SELECT (in edit) saves and shows VALUE SAVED.
RESET returns the system to the welcome screen.

## Slide 15
UNIVERSITY OF DODOMA
RELIABLE INPUT
Button Handling & Debounce
LCD-Based Menu Navigation & Parameter Setting System
15 / 20
Active-Low Wiring
Buttons connect the pin to GND; internal pull-ups hold it HIGH when idle.
Debouncing
Each press is confirmed over several samples to reject switch bounce and noise.
Edge Detection
Release flags ensure one action per press — no repeated triggering.
State-Aware Actions
The same button behaves differently in menu vs. edit mode.

## Slide 16
UNIVERSITY OF DODOMA
VIRTUAL TESTING
SimulIDE Simulation
LCD-Based Menu Navigation & Parameter Setting System
16 / 20
The full circuit is built and tested in SimulIDE before hardware, with each case screenshotted.
Power ON → Welcome message appears
Menu pressed → Main menu appears
Up / Down → Selection moves up/down
Select → Parameter screen opens
Save / Increase → Value changes or saves
Invalid action → Buzzer error indication
Reset → Back to welcome screen
Screenshots → Captured for the repository

## Slide 17
UNIVERSITY OF DODOMA
DEBUGGING JOURNEY
Troubleshooting Notes
LCD-Based Menu Navigation & Parameter Setting System
17 / 20
Key issues found and fixed while getting the buttons and display to work.
Button logic polarity
Match code to wiring: active-LOW (to GND) with pull-ups, or active-HIGH with pull-downs — never mix them.
Series resistor error
A 10k resistor in series with the button forms a divider with the pull-up, so the pin never reads a valid LOW. Connect buttons directly to GND.
Clock (F_CPU) mismatch
Internal RC defaults to 1 MHz. If F_CPU says 8 MHz, every delay is 8× off. Match F_CPU to the real clock.
LCD contrast
A blank screen usually means the contrast pot or RW-to-GND connection is missing, not a code fault.

## Slide 18
UNIVERSITY OF DODOMA
EVALUATION & DELIVERY
Assessment & GitHub Submission
LCD-Based Menu Navigation & Parameter Setting System
18 / 20
LCD & Menu
Correct pin use; clear navigation logic.
Firmware
Proper DDR/PORT/PIN and LCD handling.
Circuit & PCB
Sound wiring, routing, labels & DRC.
Repository: ATmega32_LCD_Menu_System
firmware/ (src, include, hex)
kicad/ (schematic, pcb, gerber)
simulide/ (circuit, screenshots)
documentation/ (diagrams, tests)
media/ (demo video link)
README.md + meaningful commits

## Slide 19
UNIVERSITY OF DODOMA
WRAP-UP
Conclusion & Extension
LCD-Based Menu Navigation & Parameter Setting System
19 / 20
This project delivered a complete embedded user interface on the ATmega32 — from schematic and PCB in KiCad, through firmware in MPLAB, to verification in SimulIDE.
It demonstrates LCD interfacing in 4-bit mode, reliable debounced button reading, a clear menu state machine, and user feedback through LEDs and a buzzer.
The debugging process reinforced a key lesson: hardware wiring and firmware assumptions must always agree.
Future Extension
EEPROM Parameter Storage
Save the selected parameter to the internal EEPROM so it remains available after reset or power cycling — combining menu navigation with EEPROM read/write operations for persistent settings.

## Slide 20
THANK YOU
Questions & Discussion
References
CT 321 Project 15 Brief — University of Dodoma
ATmega32 Datasheet — Microchip Technology
HD44780 LCD Controller Datasheet — Hitachi
KiCad & SimulIDE Official Documentation
The University of Dodoma · College of Informatics and Virtual Education